## Slide 1: Advanced Analytics Initial Results 2 November 2017
Digital Ventures – FitCar

## Slide 2: Executive Summary
The focus of the Advanced Analytics PoC has been to investigate how Diagnostic Trouble Codes data can be used to identify vehicles that require maintenance before the OEM recommendation.
Based on 900 vehicles live in Fitcar up to end September, we have been able to identify some specific patterns of non-critical DTC fault codes as having an elevated risk of being followed by a critical DTC fault. We were also able to identify variations between different categories of vehicles. This could be incorporated into a future release of the FitCar App to advise drivers to come in to Jiffy Lube for investigation maintenance before their engine warning light comes on.
The limited data volumes mean that we can only identify high risk vehicles in very limited scenarios. However once significantly larger volumes of data are available, this approach would enable FitCar to recommend drivers to take their vehicle to JiffyLube for diagnostics before the engine warning light comes on or it breaks down. The results could also be used to provide insight to JiffyLube on common fault patterns, enabling identification of appropriate additional services to offer (based on fixing common faults)
Although we have only spent $50k of the $120k Innovation Budget, we recommend pausing work until Q2 2018 when FitCar expect significantly more data to be available. This will enable us to fine-tune the algorithm, leverage additional data from FitCar v3, and confirm that we can generate sufficiently actionable insights to justify integrating the predictions into the FitCar app.

## Slide 3: Intelligent, Self-learning Fault Code Advisor
P0123 P0124 P0125 P0123
Vehicles generate DTC fault codes when a sensor picks up an out-of-tolerance reading. As this does not always mean there is something wrong with the vehicle, a vehicle will only notify the driver to seek maintenance when the pattern of faults meets OEM defined criteria.
Fitcar receives details of all DTC fault codes. Our analytics can identify patterns of faults that do not meet the OEM criteria to notify the driver, but which, based on historic analysis of similar vehicles that have been driven in similar conditions, have a high likelihood of being followed by subsequent more serious fault.
This could generate an additional revenue stream for JiffyLube and be a value adding feature for drivers (avoiding unexpected break downs). The data could also be used to identify common faults that JiffyLube could develop new service offerings to fix.
As more vehicles are enrolled in FitCar and more fault data becomes available, our self-learning algorithms will both become more accurate and able to assess risk in a wider range of scenarios.

## Slide 4: Initial Results
We have focussed on identifying patterns of non-critical faults that have a high likelihood of the engine warning light coming on between one hour and seven days after a non-critical fault.
We identified 30 distinct patterns that appeared in at least five vehicles.
    On average 30% of vehicles with these patterns had a critical fault within seven days
    Some patterns had a probability of 80%, some 0%
    Statistical uncertainty associated with the relatively small number of vehicles, means that we cannot be sure that some of the difference in outcomes was not simply due to chance.
    However, we were able to identify one fault code - P0171: System Too Lean (Bank 1) - that we can be statistically confident has a risk of at least 40%.
We also analysed differences based on vehicle age, mileage, engine type and OEM region
    This allows us to be statistically confident that Fault P0171 has a risk of at least 45% when seen in vehicles over 10 years old
As more data becomes available, the statistical uncertainty will reduce, enabling us to identify much high risk patterns of faults

## Slide 5: Model Output
 |  | Probability of | # of | # with | # with no |  | 95% Confidence Interval | 
Fault Code Pattern | Fault Code Description | Critical Fault | vehicles | critical fault | critical fault |  | Lower | Upper
P0420 | Catalyst System Efficiency Below Threshold (Bank 1) | 37% | 41 | 25.8 | 15.2 |  | 22% | 54%
P0300 | Random/Multiple Cylinder Misfire Detected | 37% | 32 | 20.0 | 12.0 |  | 21% | 56%
P0455 | Evaporative Emission Control System Tank Detected (gross leak) | 31% | 25 | 17.3 | 7.8 |  | 14% | 53%
P0430 | Catalyst System Efficiency Below Threshold (Bank 2) | 55% | 18 | 8.2 | 9.8 |  | 30% | 78%
P0171 | System Too Lean (Bank 1) | 68% | 16 | 5.2 | 10.8 |  | 40% | 89%
P0128 | Coolant Thermostat (Coolant Temperature Below Thermostat Regulating Temperature) | 44% | 15 | 8.3 | 6.7 |  | 19% | 72%
P0456 | Evaporative Emissions System Small Leak Detected | 40% | 14 | 8.3 | 5.7 |  | 16% | 70%
P0301 | Cylinder 1 Misfire Detected | 32% | 13 | 8.8 | 4.2 |  | 10% | 63%
P0304 | Cylinder 4 Misfire Detected | 51% | 12 | 5.9 | 6.1 |  | 21% | 80%
P0455-P0455 | pattern - see above | 5% | 11 | 10.5 | 0.5 |  | 0% | 35%
P0441 | Evaporative Emission Control System Incorrect Purge flow | 18% | 11 | 9.0 | 2.0 |  | 2% | 52%
P0302 | Cylinder 2 Misfire Detected | 36% | 11 | 7.0 | 4.0 |  | 11% | 69%
P0442 | Evaporative Emission Control System leak Detected (small leak) | 30% | 10 | 7.0 | 3.0 |  | 7% | 65%
P0133 | O2 Sensor Circuit Slow Response (Bank 1 Sensor 1) | 32% | 9 | 6.1 | 2.9 |  | 6% | 70%
P0420-P0420 | pattern - see above | 33% | 9 | 6.0 | 3.0 |  | 7% | 70%
P0303 | Cylinder 3 Misfire Detected | 13% | 8 | 7.0 | 1.0 |  | 0% | 53%
P0101 | Mass or Volume Air flow Circuit Range/Performance Problem | 29% | 7 | 5.0 | 2.0 |  | 4% | 71%
P0306 | Cylinder 6 Misfire Detected | 43% | 7 | 4.0 | 3.0 |  | 10% | 82%
P0455-P0455-P0455 | pattern - see above | 7% | 7 | 6.5 | 0.5 |  | 0% | 51%
P0401 | Exhaust Gas Recirculation Flow Insufficient Detected | 80% | 6 | 1.2 | 4.8 |  | 32% | 99%
P0102 | Mass or Volume Air Flow Circuit low Input | 50% | 6 | 3.0 | 3.0 |  | 12% | 88%
P0455-P0455-P0455-P0455 | pattern - see above | 0% | 6 | 6.0 | 0.0 |  | 0% | 47%
P0128-P0128-P0128 | pattern - see above | 22% | 5 | 3.9 | 1.1 |  | 1% | 75%
P0128-P0128 | pattern - see above | 22% | 5 | 3.9 | 1.1 |  | 1% | 75%
P0305 | Cylinder 5 Misfire Detected | 60% | 5 | 2.0 | 3.0 |  | 15% | 95%
P0457 | Evaporative Emission Control System Leak Detected | 80% | 5 | 1.0 | 4.0 |  | 28% | 99%
P0174 | System Too Lean (Bank 2) | 70% | 5 | 1.5 | 3.5 |  | 21% | 98%
P0420-P0430 | pattern - see above | 30% | 5 | 3.5 | 1.5 |  | 2% | 79%
P0139 | O2 Sensor Circuit Slow Response (Bank 1 Sensor 2) | 0% | 5 | 5.0 | 0.0 |  | 0% | 52%
P0128-P0128-P0128-P0128 | pattern - see above | 22% | 5 | 3.9 | 1.1 |  | 1% | 75%
Grand Total |  | 30% | 334 | 210.9 | 123.1 |  | 2% | 79%

## Slide 6: Detailed Model Output P0171 - System Too Lean (Bank 1)
 | Followed by critical fault |  |  | Base | 95% Confidence Interval | 
Row Labels | Yes | No | Grand Total | Probability | Lower | Upper
Over 10 |  |  |  |  |  | 
P0420 | 11.5 | 8.5 | 20.0 | 43% | 21% | 66%
P0300 | 11.0 | 9.0 | 20.0 | 45% | 23% | 68%
P0171 | 2.7 | 9.3 | 12.0 | 78% | 45% | 96%
P0128 | 3.5 | 5.5 | 9.0 | 61% | 25% | 90%
P0430 | 4.2 | 4.8 | 9.0 | 54% | 19% | 86%
P0455 | 5.0 | 4.0 | 9.0 | 44% | 14% | 79%
P0304 | 3.3 | 4.8 | 8.0 | 59% | 21% | 91%
P0133 | 4.1 | 1.9 | 6.0 | 31% | 2% | 77%
P0442 | 3.5 | 2.5 | 6.0 | 42% | 8% | 83%
P0302 | 3.0 | 3.0 | 6.0 | 50% | 12% | 88%
P0301 | 2.8 | 2.2 | 5.0 | 43% | 6% | 89%
P0401 | 0.6 | 4.4 | 5.0 | 88% | 33% | 100%
P0102 | 2.0 | 3.0 | 5.0 | 60% | 15% | 95%
 | Followed by critical fault |  |  | Base | 95% Confidence Interval | 
Row Labels | Yes | No | Grand Total | Probability | Lower | Upper
American |  |  |  |  |  | 
P0300 | 14.8 | 6.2 | 21.0 | 29% | 12% | 53%
P0455 | 12.8 | 6.3 | 19.0 | 33% | 13% | 58%
P0420 | 7.0 | 6.0 | 13.0 | 46% | 19% | 75%
P0128 | 5.5 | 5.5 | 11.0 | 50% | 20% | 80%
P0171 | 2.7 | 8.3 | 11.0 | 76% | 41% | 96%
P0455-P0455 | 8.5 | 0.5 | 9.0 | 6% | 0% | 41%
P0301 | 5.8 | 3.2 | 9.0 | 35% | 8% | 72%
P0441 | 6.0 | 2.0 | 8.0 | 25% | 3% | 66%
P0430 | 1.5 | 4.5 | 6.0 | 75% | 29% | 98%
P0304 | 2.7 | 3.3 | 6.0 | 56% | 14% | 92%
P0455-P0455-P0455 | 5.5 | 0.5 | 6.0 | 8% | 0% | 57%
P0302 | 4.0 | 1.0 | 5.0 | 20% | 1% | 72%
P0455-P0455-P0455-P0455 | 5.0 |  | 5.0 | 0% | 0% | 52%
P0133 | 3.0 | 2.0 | 5.0 | 40% | 5% | 85%
P0101 | 4.0 | 1.0 | 5.0 | 20% | 1% | 72%
P0102 | 2.0 | 3.0 | 5.0 | 60% | 15% | 95%
P0457 | 1.0 | 4.0 | 5.0 | 80% | 28% | 99%
P0442 | 2.5 | 2.5 | 5.0 | 50% | 9% | 91%
 | Followed by critical fault |  |  | Base | 95% Confidence Interval | 
Row Labels | Yes | No | Grand Total | Probability | Lower | Upper
Over 10 |  |  |  |  |  | 
American |  |  |  |  |  | 
P0300 | 8.8 | 3.2 | 12.0 | 26% | 6% | 59%
P0171 | 1.7 | 7.3 | 9.0 | 81% | 43% | 99%
P0455 | 3.5 | 3.5 | 7.0 | 50% | 14% | 86%
P0420 | 2.0 | 4.0 | 6.0 | 67% | 22% | 96%
P0128 | 1.5 | 4.5 | 6.0 | 75% | 29% | 98%
P0442 | 2.5 | 2.5 | 5.0 | 50% | 9% | 91%

## Slide 7: Recommendation
The work has shown that an Advanced Analytics approach can identify high risk patterns from DTC fault data, and could be used to inform drivers that their vehicle is at risk of developing a critical fault.
However the volume of data currently available is insufficient to generate recommendations other than in a very limited number of scenarios.
The code used to generate the results runs on a copy of the Teezle Fitcar database recreated on our developer’s workstation. We could investigate how the code could be deployed directly on to the Teezle server to enable results to be refreshed automatically as more data becomes available.
However, it is unlikely we would be able to generate usable insights until we have an order of magnitude more data available, and so recommend pausing this work until 2018. This would also allow us to incorporate additional data that will be obtained following the next release of Fitcar.

## Slide 9: Use Case: Intelligent, Self-learning Fault Code Advisor
Concept:
Advise drivers that their vehicle needs attention before the engine warning light comes on, based on a pattern of fault codes and vehicle and
driving characteristics. The solution will be self-learning, able to improve predictions as more data is collected
Approach:
1) Identify common patterns of faults that do not result in the Check Engine Light illuminating immediately
2) Identify how often each pattern results in the Check Engine Light illuminating reasonably soon after
3) Understand how the likelihood of the Check Engine Light illuminating following a particular pattern of faults varies according to vehicle / driving characteristics
4) Build a predictive model that assesses the risk that the Check Engine Light will illuminate in the near future following each non-critical fault
Core Data Requirement:
Fault codes classified as critical and non-critical.
Vehicle characteristics, Driving characteristics
Additional Data:
SME input on key risk factors to enable optimum features to be engineered for the predictive model
Likelihood of success: Medium
It should be possible to identify some high risk fault patterns that are common across a wide variety of vehicles from current data
With limited data volumes, it may not be possible to engineer an optimal set of features
Business Value: High
Provide insight to JiffyLube on common fault patterns, enabling identification of appropriate additional services to offer (based on fixing common faults)
Generate additional revenue for JiffyLubes by recommending drivers to visit JiffyLube for proactive maintenance before their vehicle develops a critical fault
Increase customer take-up and loyalty by enabling drivers to avoid the expense and inconvenience associated with an unexpected critical fault

## Slide 10: Descriptive Statistics
The analysis is based on data supplied by Teezle on 4 Oct ’17 which contains:
    1692 distinct users
    957 vehicles, registered to 940 distinct users (15 users have 2 vehicles registered, 1 has 3)
Vehicle Diagnostics table contains 19970 fault records from 10 Nov ’16 to 25 Sep ‘17, comprising:
    3120 “Check Engine” records
    10236 “Qualified DTC” records
    6614 “Pending DTC” records
There are 286 distinct fault codes, 217 of which appear with “Pending DTC” status
There are 376 distinct vehicles in the Vehicle Diagnostics table, 332 have a “Pending DTC” code
Faults are not uniformly distributed. Fifteen vehicles account for over half of all fault records. The median number of codes is ten per vehicle.

## Slide 11: Initial Model
Identify common patterns of faults where a series of non-critical faults is followed by a critical fault
Identify all faults with status “Pending DTC” and classify these as non-critical
    Exclude any faults that appear immediately after a “Qualified DTC” or “Check Engine” fault (these may be directly related)
    Exclude any faults that occur less than an hour before a “Qualified DTC” or “Check Engine” fault (the driver would not be able to act on the prediction)
    Identify whether the fault is followed by a critical fault within a week (longer than this may mean the critical fault is unrelated)
For each fault from step 1, identify other non-critical faults that occurred up to a week before but not before a critical fault
Identify all distinct patterns of faults from step 2 (but ignoring the order than the faults appear in)
Identify the common non-critical fault patterns and the probability that they result in a critical fault, adjusting for duplication where the same pattern repeats in the same vehicle.

## Slide 12: Illustration
Y
X
B
D
F
Day 1 Day 2 Day 3 Day 4 Day 5 Day 6 Day 7 Day 8 Day 9 Day 10 Day 11 Day 12
A
E
G
C
Code | Include in analysis? | Critical fault within a week? | Non critical faults in previous 7 days & after previous critical fault
A | Yes | Yes (X) | 
B | No, too soon after critical fault X |  | 
C | Yes | No | 
D | Yes | No | D
E | Yes | Yes (Y) | C,D
F | Yes | Yes (Y) | D,E
G | No, too close to critical fault Y |  | 
Pattern | Followed by Critical Fault within 7 days?
A | Yes
C | No
D | No
CD | No
E | Yes
DE | Yes
CDE | Yes
F | Yes
EF | Yes
DEF | Yes

## Slide 13: Results – all vehicles
30 fault patterns appear on at least five vehicles.
22 of these “patterns” consist of a single fault, but 8 include multiple faults.
7 patterns have a greater than 50% chance of being followed by a critical fault, however the small sample size means that this may be a coincidence.
Using standard statistical assumptions, there are no patterns that we can be confident have a greater than 40% chance of being followed by a critical fault

## Slide 14: Results – disaggregating by vehicle characteristics
The risk of a non-critical fault being followed by a critical fault is likely to vary depending on the vehicles characteristics and history. However analysing subsets of vehicles reduces the sample size, making it more difficult to distinguish between high risk fault patterns and coincidences.
Our analysis has included some simple groupings based on easily available data that intuitively feel as though they could influence engine fault behaviour:
    Vehicle Age (0 to 5, 5-10, 10+)
    Vehicle Mileage at last service (< 100k, 100-150k, 150k+)
    OEM home region (Asia, Europe, America)
    Engine cylinder count
Looking at fault pattern P0171, we can see that this can increase the statistical confidence that a fault pattern has a high risk of being followed by a critical fault:
  Fault P0171 occurs on 12 vehicles over 10 years old, and was followed by a critical fault in 78% of cases. Using standard statistical assumptions, we can be confident the risk as at least 45%, slightly higher than the 40% when looking across all vehicles.
  The same fault occurs on 11 vehicles where the OEM is American, and was followed by a critical fault in 76% of cases, and we can be confident that the risk is at least 41%
  Combining these, fault P0171 occurs on 9 vehicles that are over 10 years old with an American OEM, and was followed by a critical fault in 81% of cases. However, the reduced number of vehicles means that we can only be confident that the risk is at least 43%, slightly lower than when looking across all vehicles over 10 years old.

## Slide 15: Future Direction
Investigate alternatives to the “one hour” and “one week” time window
    Consider mileage based thresholds
    Should be driven by data (i.e. how long is the risk of a critical fault elevated following a non-critical fault)
Investigate other features that could predict the risk of a critical fault
    Based on driving behaviour / environment
        E.g. are some patterns much higher risk in vehicles that do mainly city driving (low speed shorter journeys) vs vehicles that do mainly freeway driving (higher speed longer journeys)
Investigate other elements of fault patterns
    Time / mileage between faults
        e.g. does having a fault 3 times in an hour mean a higher/lower risk than seeing the same fault 3 times spread over a week?
    Order of faults
        e.g. does fault A followed by fault B have the same risk as seeing fault B followed by fault A?
Investigate excluding non-critical faults that occur after a unresolved critical fault